ULTRASEAL® AB WATERPROOFING DIRECTIVES FOR SHOTCRETE PROPERTY LINE FOUNDATIONS UNDER NON-HYDROSTATIC CONDITIONS

The accompanying guide specification has been prepared according to the principles established in the Manual of Practice published by the Construction Specification Institute. This guide specification is intended to be adapted by the design professional to suit the requirements of individual projects. This specification provides an outline covering Parts 1, 2, & 3 with specific information about standards, quality assurance, product description, warranty requirements, and application. Specifically, Part 3, Execution, contains special installation and application guidance of the ULTRASEAL AB Waterproofing System when used with below-grade shotcrete foundations planned for non-hydrostatic conditions.

The waterproofing directives for shotcrete should be utilized to coordinate with related specification sections and then deleted prior to finalizing the specification. This shotcrete waterproofing directive is provided prior to the guide specification in three parts as follows:

        - SHOTCRETE SUMMARY

SPECIFICATION COORDINATION – conveying important directives that should appear in other pertinent Sections of the Project Specifications Documents.

HYDROSHIELD WARRANTY REQUIREMENTS FOR SHOTCRETE PROPERTY LINE FOUNDATIONS UNDER NON-HYDROSTATIC CONDITIONS – Warranty requirements for projects participating in the HydroShield Quality Assurance Program (HSQAP)

SHOTCRETE SUMMARY

Shotcrete is concrete pneumatically projected onto a surface at high velocity. It is typically blown through a hand-held nozzle, where water is added to the small aggregate concrete mix just prior to being applied and consolidated. Using shotcrete for constructing property line below-grade structural walls has become more common over the last ten years. Shotcrete typically costs less and takes less time to complete than a comparable sized cast-in-place concrete project.

However, application of shotcrete can create difficult conditions for insuring the performance of below-grade waterproofing systems. Improperly mixed or placed shotcrete can, among other problems, create voids between the shotcrete and the waterproofing membrane, develop shadow voids or poor consolidation behind steel reinforcement, excessive cracking due to low moisture content, improper cleaning during application can produce rebound pockets, unbonded areas, sags and other defects, and overspray contamination can minimize the excellent structural bond that occurs between the ULTRASEAL AB membrane surface and shotcrete.

Unlike cast-in-place concrete, the success in applying shotcrete is mostly dependent on the skill and experience of the shotcrete installation crew, especially the nozzleman. Although it may be reassuring to have a properly qualified nozzleman on the project, it cannot be assumed that the quality of in-place shotcrete will be consistently good unless there is continued attention to, and inspection of, the preparation of

substrate surfaces to receive shotcrete, the position, size and anchorage of steel reinforcement, material quality, mixing of materials, equipment operation and gunning technique, removal of rebound and sand pockets, encapsulation of steel reinforcement, and proper curing.

Furthermore, even properly applied shotcrete is more likely to develop shrinkage cracks than cast-in-place concrete during curing due to the lower water to cement ratio, and the lack of actual field practice of moisture curing the shotcrete for several days as recommended in American Concrete Institute (ACI) 506.2-16.

To address the difficult conditions of waterproofing shotcrete, CETCO has developed special product installation guidelines and drafted specification coordination directives for design professionals to consider when specifying the ULTRASEAL AB System to waterproof below-grade, blind-side shotcrete foundations.

SPECIFICATION COORDINATION

Section 07 17 00 defines the requirements for the ULTRASEAL AB waterproofing system that includes an initial course of AQUADRAIN 15XP installed over the shoring wall. Most projects require coordination with several other Sections of the Project Specifications to assure proper waterproofing system installation and to meet the requirements for the issuance of the Manufacturer’s HydroShield Quality Assurance Program Warranty (HydroShield Warranty). Following are the typical Specification Sections pertinent to coordinate with Section 071700 that CETCO recommends the project design team review and include the following directives in the project design and specifications:

SECTION 31 66 16 – Special Foundation Walls: Shoring and Cementitious Protection Board

        - Specify that the wood lagging shoring is carried to the lowest level of the waterproofing installation. Require that the lagging boards be tight together and secure enough to receive the shotcrete application against the waterproofing system. Require that voids and cavities exterior of the lagging be filled with engineered soil or cementitious grout.

As part of the waterproofing Work, specify that 12 mm (½”) cementitious wall board be installed over the top end of each metal soldier pile prior to installing the waterproofing system. Cementitious wall board will function as a protection course during the excavation and removal of the top several feet of the metal soldier pile and wood lagging as required by local building codes.

SECTION 03 15 13 – Concrete Joint Waterstops

        - HydroShield Warranty requires the application One (1) row of CETINJECT Injectable Waterstop and one (1) row of WATERSTOP-RX shall be installed in the base wall to slab or footing joint. All other shotcrete construction joints require the application of two (2) rows of WATERSTOP-RX in all horizontal and vertical shotcrete construction stop joints, require concrete surface to be reasonably smooth, such as a float finish or formed surface.

HydroShield Warranty requires the application of one (1) strip of WATERSTOP-RX in all shotcrete lift joints after the joint surface has been cleaned of rebound, poorly bonded material, laitance, or any other defect. Secure by pushing WATERSTOP-RX half-way down into fresh shotcrete.  For shotcrete surfaces specified to be very rough to enhance interlocking with the succeeding shotcrete placement, require that a 38 mm (1-1/2”) wide strip of flat surface be tooled or formed into the shotcrete surface to facilitate proper installation of the waterstop. Maintain a 75 mm (3”) minimum embedment depth to exterior face of concrete.

HydroShield Warranty requires the application of one (1) strip of WATERSTOP-RX around all mechanical penetrations extending through the shotcrete foundation.

HydroShield Warranty requires the application of a 9 mm (3/8”) bead of AKWASWELL and one (1) strip of WATERSTOP-RX around all steel reinforcement anchorage.

WATERSTOP-RX is not designed for use in expansion joints. Expansion joints should be sealed with proper CETCO CXJ Expansion Joint product.

SECTION 03 30 00 – Cast-in-Place Concrete (Columns and Pilasters)

        - Concrete work should use conventional cast in place forms that produce a smooth surface. Do not use stay-in place concrete forming; use removable forming products only.

SECTION 03 37 13 – Shotcrete (Wet Mix Shotcrete / Pneumatically-Placed Concrete)

        - It is important that all the elements which will aid in providing a well-designed and correctly executed shotcrete job be written into the specification. Specification should explicitly detail type of shotcrete process (wet mix only), contractor and nozzleman experience and qualifications, materials, design mix, admixtures, acceptance/rejection criteria, quality and method of substrate preparation, steel reinforcing details and anchorage, construction joints, finish, curing procedure, and testing requirements.

Specify that wet mix shotcrete walls be placed in strict accordance with ACI 506.2-13, which includes, but not limited to, gunning all walls from the bottom up to their full design thickness in a single application, minimizing the lift height, dampening absorptive substrates before placing shotcrete, removing rebound and sand pockets, properly encasing steel reinforcement, and properly curing the shotcrete installation.

Specify a shotcrete subcontractor qualification submittal. Require the shotcrete subcontractor to have a minimum of three (3) years successful experience in structural shotcrete work of similar scope, wet mix type, and project size.

Specify a shotcrete crew qualification submittal. Require shotcrete subcontractor to submit written evidence giving qualifications and experience of foreman, delivery equipment operator, nozzle helper (rebound cleaner), and nozzleman certifying that each has experience with the specified shotcrete mix type and the application technique required for the Work. Require that the nozzleman be an ACI-certified Shotcrete Nozzleman (Wet-Mix Process) or other equivalent certification.

Specify Quality Assurance panel mock-up test conducted with the waterproofing applied to the substrate. Cores should be taken of the mock-up and analyzed to ensure that the shotcrete conforms to Core Grade 1 or 2 as defined in ACI 506.2-95 Section 1.7.

In accordance with project requirements, construct test panel using the same equipment, materials, and mix proportions, typical reinforcement, waterproofing membrane system substrate proposed for the Project. Conduct test utilizing each shooting position expected in the Work.

Conduct panel test where two lifts of shotcrete are applied.

Three (3) days after shotcrete is placed, a minimum of six 100 mm (4”) diameter cores through the test panel shall be taken by the Owner’s testing agency. The cores shall cut near the rebar for visual inspection to determine shotcrete core grade of Grade 1 or Grade 2 as defined in ACI 506.2-95, Section 1.7. If the shotcrete core grade is worse than a Grade 2, the Quality Assurance Manager should require another mock-up test until satisfactory results are achieved.

Application of shotcrete in the Work shall not proceed until the test panels have been inspected, cored, tested, and approved.

Specify as part of the shotcrete work, the installation of temporary protective sheeting (min. 450 mm (18”)) over adjacent substrate areas, including above shotcrete lift lines during application, to provide protection from shotcrete overspray contamination. It is extremely important to keep the overspray from contaminating (coating) the surface of the ULTRASEAL AB. Protective sheeting should be employed above and aside all known shotcrete lift stops, as well as horizontal and vertical construction stops. Protective sheeting must be removed prior to application of succeeding shotcrete lift or construction area. Specify any rebound or overspray from previously applied area must be removed prior to succeeding shotcrete placement. Protective sheeting materials include, but may not be limited too, 1.5 mm (6-mil) Visqueen, geotextiles, felt, and construction paper.

Specify that the wet mix shotcrete walls should be gunned to their full design thickness in a single application and not gunned in layers, thereby reducing the possibility of cold joints and laminations. Where a finer interior finish is desired a thin “flash finish” coat may be applied.  ACI 506R-16 Section 3.5 provides guidance for finish coats.

Specify the maximum shotcrete lift height and the minimum interval cure time between succeeding shotcrete lift. Specify that the shotcrete lift joints do not match the ULTRASEAL AB membrane overlap edges. Experience has shown to limit the practical shotcrete lift heights to less than 1.2 m (4’) and require sufficient time between lifts to allow the applied shotcrete to set.

Specify as part of the steel reinforcement work, rebar anchorage shall be “all-thread or threaded rod” with a 25 mm (1”) fender washer and wing nut assembly to compress and hold the AKWASWELL and WATERSTOP-RX around outer end of rod against the waterproofing membrane.

Require that expanded metal stay-in-place forming not be used to form shotcrete construction stops. Stay-in-place forming can be an unstable substrate to shoot shotcrete against, thus creating voids or poor consolidation. Use solid removable wood or metal forms to provide stable form edge for shotcrete construction stops.

One (1) row of CETINJECT Injectable Waterstop and one (1) of WATERSTOP-RX shall be installed in the base wall to slab or footing joint.

Specify as part of the shotcrete Work, the installation of two (2) rows of WATERSTOP-RX at all construction cold joints. Applicable construction cold joints include the shotcrete wall to slab/footing; vertical formed work edge joints; shotcrete to cast-in-place columns; and daily shotcrete lift joint stops.

Specify as part of the shotcrete work, the installation of one WATERSTOP-RX strip into each shotcrete lift joint, regardless of whether the wall will encounter hydrostatic or non-hydrostatic conditions.

Require that shotcrete operations should be suspended during high winds, rain, or near freezing temperatures.

Require placement of wet mix shotcrete first in corners, recesses, and other areas where rebound or overspray cannot escape or be removed easily.

Specify that the Owner shall hire an independent, third party inspection service to monitor the waterproofing and shotcrete installation to ensure that both the waterproofing and shotcrete are being applied as specified and administer a shotcrete quality control/quality assurance testing program.

HYDROSHIELD WARRANTY REQUIREMENTS FOR SHOTCRETE PROPERTY LINE FOUNDATIONS UNDER NON-HYDROSTATIC CONDITIONS

The specification coordination directives and Section 07 17 00 Guide Specification herein provide the construction documents framework for a successful ULTRASEAL AB waterproofing system application with wet mix shotcrete foundation walls planned for hydrostatic conditions. All projects that intend to apply for HydroShield Warranty covering both the material and labor must meet the following:

        - Utilize the directives and guide specification herein as a basis of design and product application.

        - CETCO Approved Applicator must install the waterproofing and AQUADRAIN system.

AQUADRAIN system shall be connected to an operative water discharge system.

Single strip of WATERSTOP-RX shall be installed in all shotcrete lift joints.

One (1) row of CETINJECT Injectable Waterstop and one (1) row of WATERSTOP-RX shall be installed in the base wall to slab or footing joint. Two (2) rows of WATERSTOP-RX shall be installed in all other shotcrete construction joints.

Require Owner’s independent inspector to inspect the waterproofing installation just prior to shotcrete application to ensure that the waterproofing has not been damaged during steel reinforcement and anchorage installation.

Concrete work shall use conventional cast-in-place forms that produce a smooth surface. Do not use stay-in place concrete forming; use removable forming products only.

All CETINJECT Injectable Waterstops must be injected with CETCO AKWASEAL chemical grout after allowing the concrete to cure for a minimum of 28 days and/or after the site engineer provides approval.

SECTION 07 17 00

ULTRASEAL® AB WATERPROOFING SYSTEM

FOR SHOTCRETE PROPERTY LINE FOUNDATION WALLS UNDER NON-HYDROSTATIC CONDITIONS

< Notes to Specifier:

          - For below-grade cast-in-place applications refer to CETCO’s Master Guide Specification for ULTRASEAL AB Waterproofing System. >

- GENERAL

      - SUMMARY

        - The work of this section includes, but is not limited to the furnishing and installing the following materials, per project specifications and drawings, or as directed by waterproofing manufacturer:

          - ULTRASEAL AB Waterproofing Membrane with all applicable accessory products

AQUADRAIN® Prefabricated drainage composite and AQUADRAIN 100BD Base Drain

      - RELATED DOCUMENTS

All the contract documents, including General and Supplementary General Conditions and Division 1 General Requirements, apply to the work of this section.

Shotcrete reference documents:

ACI 506R-16 - Guide to Shotcrete

ACI 506.2-13 - Specification for Shotcrete (Reapproved 2018)

ACI 506.4-94 - Guide for Evaluation of Shotcrete (Reapproved 2004)

ACI 506.6T-17 – Visual Shotcrete Core Quality Evaluation

RELATED SECTIONS

Carefully examine all of the Contract Documents for requirements which affect the work of this section.

Other specification sections which directly relate to the work of this section include, but are not limited to, the following:

Section 02 30 00 - Subsurface Investigation

Section 02 32 00 - Geotechnical Investigations

Section 03 15 13 - Waterstops

Section 03 30 00 - Cast-In-Place Concrete

Section 03 37 13 - Shotcrete

Section 07 21 00 - Thermal Insulation

Section 07 60 00 - Flashing and Sheet Metal

Section 07 90 00 - Joint Protection

Section 07 95 00 - Expansion Control

Section 22 00 00 - Plumbing

Section 23 00 00 - Heating, Ventilation, and Air Conditioning (HVAC)

Section 26 00 00 - Electrical

Section 31 00 00 - Earthwork

Section 31 23 00 - Excavation and Fill

Section 31 41 00 - Shoring

Section 31 66 16 - Special Foundation Walls

Section 33 41 00 - Subdrainage

REFERENCES

Materials, equipment and methods will comply with American Standards, or other International standards or codes of practice, as identified in this Specification or in other relevant specifications. The standards will be current at the date of signing the contract for the project.

The Contractor may propose the adoption of alternative standards and will provide comprehensive details and explanations with any proposals. The use of alternative standards will be subject to the approval of the Engineer.

ASTM Standards

ASTM C 836 - Standard Specification for High Solids Content, Cold Liquid-Applied Elastomeric Waterproofing Membrane for Use with Separate Wearing Course

ASTM D 903 (Mod.) - Standard Test Method for Peel or Stripping Strength of Adhesive Bonds

ASTM D 4632 - Standard Test Method for Grab Breaking Load and Elongation of Geotextiles

ASTM D 4833 - Standard Test Method for Index Puncture Resistance of Geomembranes and Related Products

ASTM D 5084 - Standard Test Methods for Measurement of Hydraulic Conductivity of Saturated Porous Materials Using a Flexible Wall Permeameter

ASTM D 5385 (Mod.) - Standard Test Method for Hydrostatic Pressure Resistance of Waterproofing Membranes

ASTM E 96 B - Standard Test Methods for Water Vapor Transmission of Materials

ASTM E 154 - Standard Test Methods for Water Vapor Retarders Used in Contact with Earth Under Concrete Slabs, on Walls, or as Ground Cover

SYSTEM DESCRIPTION

Furnish and install a waterproofing system and prefabricated drainage composite system to prevent the passage of liquid water and install without defects, damage or failure. Waterproofing shall be an active-polymer core with adhesive bond technology and all applicable accessory products.

SUBMITTALS

General: Prepare and submit specified submittals in accordance with "Conditions of the Contract" and Division 1 Submittals Sections.

Product Data: Submit manufacturer’s product data, with complete general and specific installation instructions, recommendations, and limitations.

Product Samples: Submit representative samples of the following for approval:

ULTRASEAL AB Waterproofing Membrane

AQUADRAIN 100BD Base Drain and AQUADRAIN 15XP Prefabricated Drainage Composite

Waterproofing Material and Labor Warranty: At time of bid, submit a sample copy of the Manufacturer’s Waterproofing warranty complete with all coverage’s, limitations, and conditions.

Material Certificates: Submit certificate(s) by manufacturer certifying materials comply with specified performance characteristics and physical requirements. Submit certification that waterproofing system and components, and protection materials are supplied by a single-source manufacturer.

Contractor Certificate: At time of bid, submit written certification that installer has current Approved Applicator status with waterproofing material manufacturer.

QUALITY ASSURANCE

Installer Qualifications: Installing company should have at least three (3) years’ experience in work of the type required by this section, who can comply with manufacturer's warranty requirements, and who is an Approved Applicator as determined by waterproofing/drainage system manufacturer.

Manufacturer Qualifications:  Waterproofing membranes and all accessory products shall be provided by a single manufacturer with a minimum of 40 years’ experience in the direct production and sales of waterproofing systems. Manufacturer shall be capable of providing field service representation during construction, approving an acceptable installer, and recommending appropriate installation methods.

Pre-Installation Conference: A pre-installation conference (pre-con) shall be held at least two weeks prior to commencement of field installation to establish procedures to maintain required working conditions and to coordinate this work with related and adjacent work. Confirm that all parties understand what is required to provide a substrate that is suitable to receive the Waterproofing System. Verify that final waterproofing and waterstop details comply with waterproofing manufacturer's current installation requirements and recommendations. Pre-con meeting attendees should include representatives for the owner, architect, inspection firm, general contractor, waterproofing contractor, concrete contractor, excavating/backfill contractor, and mechanical and electrical contractors if work penetrates the waterproofing.

Materials: Obtain waterproofing membrane with accessory products and prefabricated drainage materials from a single manufacturer to assure material compatibility.

Independent Inspection: Owner shall make all arrangements and payments for an independent inspection service to monitor waterproofing material installation compliance with the project contract documents and manufacturer’s published literature and site-specific details. Independent Inspection Firm shall be an approved company participating with the waterproofing manufacturer’s Certified Inspection Program. Inspection service shall produce reports and digital photographs documenting each inspection. Reports shall be made available in a timely manner to the contractor, waterproofing installer, waterproofing material manufacturer, and architect. Inspections should include substrate examination, beginning of waterproofing installation, periodic intervals, final inspection prior to concrete or backfill placement against the waterproofing, during expansion joint installation, and field fabricated splices of expansion joint.

Water Sample Test: Waterproofing contractor shall supply project site water sample to waterproofing membrane manufacturer for analysis. Manufacturer shall conduct test free of charge. Contractor is responsible for collection and shipment of 1.8 L (64 oz) of actual site water. Water should be shipped in uncontaminated, sealed plastic container to: CETCO, Attn: BMG Field Services, 2870 Forbs Ave, Hoffman Estates, IL 60192. Also provide project name, city, and state along with return address to forward test results.

DELIVERY, STORAGE, AND HANDLING

Delivery and Handling: Deliver materials in factory sealed and labeled packaging. Sequence deliveries to avoid delays, while minimizing on-site storage. Handle and store following manufacturer's instructions, recommendations, and safety data sheets. Protect from construction operation related damage, as well as damage from weather, excessive temperatures and prolonged sunlight. Remove damaged material from site and dispose of in accordance with applicable regulations.

Storage: Do not double-stack pallets during shipping or storage. Protect waterproofing materials from moisture, excessive temperatures and sources of ignition. Provide cover, top and all sides, for materials stored on-site, allowing for adequate ventilation.

PROJECT CONDITIONS

Substrate Condition: Proceed with work only when substrate construction and preparation work is complete and in condition to receive waterproofing system. All plumbing, electrical, mechanical, and structural items to be under or passing through the waterproofing shall be positively secured in their proper positions prior to waterproofing system installation. Substrate preparation shall be per waterproofing manufacturer’s guidelines.

Weather Conditions: Perform work only when existing and forecasted weather conditions are within the guidelines established by the manufacturer of the waterproofing materials. Do not apply waterproofing materials in areas of standing or active water, or over ice and snow. Though exposure to precipitation and ground water seepage typically will not adversely affect ULTRASEAL AB, the General Contractor shall maintain site conditions to remove standing water from precipitation or ground water seepage in a timely manner. Should ULTRASEAL AB be subjected to pre-hydration because of prolonged immersion, inspection (independent inspector) of the material and written acceptance from CETCO is required prior to concrete or backfill placement. Contact waterproofing manufacturer for guidance.

WARRANTY

Warranty eligibility for the project must be validated by Manufacturer, confirming acceptance of the installation and independent inspection reports are in accordance with the manufacturer’s quality assurance program requirements.

Waterproofing Material and Labor Warranty: Upon installation completion and manufacturer acceptance of the work required by this section, the waterproofing materials manufacturer will provide to the project Owner, a written five (5) year non-prorated warranty, covering both materials and labor. Issuance of Manufacturer's Waterproofing Warranty requires the following: (1) Waterproofing System products and drainage composite products shall have been provided by a single manufacturer; (2) Installation of waterproofing products and CXJ Expansion Joint by Manufacturer's Approved Applicator in full accordance with the manufacturer’s quality assurance program requirements, including additional shotcrete requirements addressed herein; (3) Installation inspected by an approved and trained Independent Inspection Firm participating with the waterproofing manufacturer’s Certified Inspection Program; (4) In Division 3 work, one (1) row of CETINJECT and  one (1) row WATERSTOP-RX must be installed in the base wall to slab or footing joint. Two (2) rows of WATERSTOP-RX shall be installed in all other shotcrete construction joints. WATERSTOP-RX shall be installed around applicable penetration and structural members. Manufacturer's warranty shall be independent from any other warranties made by the Contractor under requirements of the Contract Documents and may run concurrent with the other warranties.

PRODUCTS

MANUFACTURERS

Colloid Environmental Technologies Company (CETCO)

2870 Forbs Avenue, Hoffman Estates, Illinois 60192 USA

800-527-9948 Toll free; 847-851-1800 Phone

http://www.cetco.com/BMG

MATERIALS

ULTRASEAL AB MEMBRANE: 2.3 mm (100-mil) thick composite membrane comprised of a polyethylene liner and an advanced Active Polymer Core (APC) layer integrally bonded to an aggressive pressure sensitive adhesive that locks the membrane to concrete. ULTRASEAL AB applications include under slab, property line retention walls, backfilled walls, and earth covered structures. Roll size: 1.22 m x 7.62 m (4.0′ x 25.0′)

ULTRASEAL AB performance properties:

| PROPERTY | TEST METHOD | TYPICAL VALUE |
| --- | --- | --- |
| Hydrostatic Pressure Resistance | ASTM D 5385 mod. | 70 m (231 ft.) |
| Permeability | ASTM D 5084 | <1 x 10-11 cm/sec. |
| Peel Adhesion to Concrete | ASTM D 903 mod. | 2.6 kN/m (15 lbs./in) |
| Grab Tensile Strength | ASTM D 4632 | 667 N (150 lbs.) |
| Puncture Resistance | ASTM D 4833 | 311 N (70 lbs.) |
| Elongation | ASTM D 4632 | 50% |
| Crack Bridging | ASTM C 836 | Passed |
| Resistance to Decay | ASTM E 154 | Passed |
| Permeance | ASTM E 96 B | 0.03 Perms |

ACCESSORIES

Adhesives & Tapes:

CETSEAL:  A multipurpose UV stable single component polyether moisture cure sealant / adhesive.

SEAMTAPE: 75 mm (3”) wide rubber-based sealant tape

Grade Terminations:

ENVIROSHEET/ENVIROSHEET LT: Self-adhering flashing membrane used for grade and thru-wall detailing. <Refer to CETCO’s Guide Specification for ENVIROSHEET/ENVIROSHEET LT>

M-2000 LIQUID FLASHING: Trowel-grade, urethane detailing mastic.

Miscellaneous:

AKWASEAL LV: Low Viscosity hydrophobic polyurethane chemical grout

AKWASEAL FLEX: Flexible hydrophobic polyurethane chemical grout

AKWASWELL: Hydrophilic polyurethane caulk used for detail work.

BENTOSEAL: Trowel-grade, bentonite/butyl-rubber detailing mastic.

HYDROBAR TUBES: 50 mm (2”) diameter x 60 cm (2’) long, water soluble tube container filled with active granular material.

TB-BOOT: Pre-formed, single piece thermoplastic cover for tie-back heads and soil nails. Four sizes available: TB-3, TB-6SN, TB-8, and TB-10.

WATERSTOPPAGE: 22.7 kg (50 lbs.) bag of active granular material.

Expansion Joints:

CXJ-200/400: An extruded thermoplastic expansion joint product consisting of a 50 mm (2”)/ 100 mm (4”) wide dual-cell center gland with two integrated flashing flanges on both sides of the center gland. <Refer to CETCO’s Guide Specification for CXJ-200/400>

Waterstops:

WATERSTOP-RX: <Refer to CETCO’s Guide Specification for WATERSTOP-RX>

WATERSTOP-RX 101 – 25 mm (1”) x 20 mm (3/4”) x 5 m (16’8”) rolls of a flexible strip of bentonite and butyl rubber compound for use in concrete construction joints - not designed for expansion joints.

WATERSTOP-RX 101T – 31 mm (1-1/4”) x 12 mm (1/2”) 6 m (20’) trapezoidal rolls of flexible strip of bentonite and butyl rubber compound with a reinforcing poly scrim for use in concrete construction joints - not designed for expansion joints.

WATERSTOP-RX 102 – 20 mm (3/4") x 9 mm (3/8") x 10 m (33'4”) rolls of flexible strip of bentonite and butyl rubber compound for use in concrete construction joints - not designed for expansion joints.

AKWASTOP: 20 mm (3/4”) x 10 mm (3/8”) x 10 m (33’) rolls of a flexible strip of hydrophilic rubber for use in concrete construction joints - not designed for expansion joints. <Refer to CETCO’s Guide Specification for AKWASTOP>

CETINJECT: Waterstop injection hose system consisting of an 11 mm (7/16”) diameter hose that functions as a delivery channel for CETCO AKWASEAL waterproofing resins. <Refer to CETCO’s Guide Specification for CETINJECT>

Drainage Composites:

AQUADRAIN 15XP: 1.2m x 15.8m (4-ft x 52-ft) roll of a three-dimensional polypropylene drainage core with a nonwoven geotextile adhered to one side to allow water passage while restricting soil particles. Composite includes a thin polyethylene sheet on the back of the drainage core.

AQUADRAIN 100BD Base Drain: 25 mm (1”) thick x 300 mm (12”) high base drain composite designed to collect water from sheet composite drainage and then discharge the water to proper sump system or gravity to daylight.

Compressive Strength, 457 kPa (10,000psf);

Water Flow Capacity, 1,197 l/m/m (97gpm/ft);

Thickness, 25 mm (1”)

EXECUTION

INSPECTION

Comply with contract documents and manufacturer's product data, including product application and installation instructions.

The installer, with the Owner’s Independent Inspector present, shall examine conditions of substrates and other conditions under which this section work is to be performed and notify the contractor, in writing, of circumstances detrimental to the proper completion of the work. Do not proceed with work until unsatisfactory conditions are corrected and are acceptable for compliance with manufacturer's warranty requirements. General substrate conditions acceptable for the waterproofing installation are listed below. For conditions not covered in this Section, contact the waterproofing manufacturer for guidance.

WORKING MUD SLAB: Working concrete mud slabs should have a float finish to provide a planar surface; without sharp angular depressions, voids, or raised features.

COMPACTED SOIL OR GRAVEL SUB-GRADE: Sub-grade shall be compacted to a minimum Modified Proctor compaction of 85% or greater as specified by civil/geotechnical engineer. The finished sub-grade surface shall be well-leveled, uniform, and free of debris and standing water or ice. Aggregate sub-grades shall consist of 20 mm (¾”) stone or smaller and rolled flat, free from any protruding sharp edges. Specific sub-grade materials/specifications shall be designed and approved by the project’s civil or geotechnical engineer.

WOOD TIMBER SHORING: Wood lagging shoring should extend to the lowest level of the waterproofing installation with any voids or cavities exterior of the lagging timbers filled with compacted soil or cementitious grout. Interior surface of lagging boards should be planar and tight together with gaps less than 25 mm (1”). Gaps in excess of 25 mm (1”) should be filled with cementitious grout, compacted soil, wood, extruded polystyrene (25 psi min) or CETCO approved polyurethane spray foam (20 psi min). Do not use plywood or other surface treatment over large lagging gaps that leave the cavity void. In areas where lagging gaps are 63 mm (2-1/2”) or less, AQUADRAIN sheet drainage can be installed over lagging to provide uniform surface to mount the waterproofing without requirement of filling gaps (voids or cavities exterior of the lagging timbers shall still be filled with compacted soil or cementitious grout). AQUADRAIN sheet and 100BD base drain system should be connected to an operative water discharge system. All lagging board nails and other mechanical projections shall be removed or pounded flush. In areas where AQUADRAIN drainage composite is not utilized, install a protection material over all soldier piles with raised lagging hanger bolts, form tie rods, or other irregular surface; protection material should extend a minimum 150 mm (6”) to both sides of the steel piling.

CUT ROCK FACE, AUGER CAST CAISSON, OR SHOTCRETE SHORING WALLS: Interior surface of cut rock, auger cast caisson, or shotcrete shoring walls should be planar without irregular surface conditions, voids, and sharp transitions that would leave a void space to the outside of the drainage and waterproofing installation. Irregular rock, void pockets, cracks, sharp concave transitions should be completely filled or smoothed with cementitious grout, shotcrete, or other approved solid material.

MECHANICAL OR OTHER PENETRATIONS: Mechanical, structural, or architectural materials that will pass through the plane of the waterproofing membrane shall be properly installed and secured in their final position prior to installation of the waterproofing system.

CONCRETE:  Concrete to be waterproofed shall be properly placed and consolidated. Reinforced structural slabs should be a minimum of 150 mm (6") thick when placed on a working mud slab. Reinforced concrete slab(s) on compacted grade shall be a minimum of 100 mm (4”) thick. When hydrostatic conditions exist, install ULTRASEAL AB under all footings, elevator pits and grade beams. Cast-in-place concrete to receive waterproofing shall be of sound structural grade with a smooth finish, free of debris, oil, grease, laitance, dirt, dust, or other foreign matter which will impair the performance of the waterproofing and drainage system and which do not comply with manufacturer's warranty requirements. ULTRASEAL AB can be installed on green structural concrete as soon as the forms are removed provided the contractor gains written approval from project structural engineer listing any site-specific concrete curing time requirement. Do not apply ULTRASEAL AB waterproofing directly over lightweight insulating concrete, wood, or steel decking.

Remove dirt, debris, oil, grease, cement laitance, or other foreign matter which will impair or negatively affect the performance of the waterproofing and drainage system.

Protect adjacent work areas and finished surfaces from damage or contamination from waterproofing products during installation operations.

Form fins, ridges, ponding ridges and other protrusions should be level and smooth with concrete surface.

Honeycombing, aggregate pockets, and other voids shall be completely filled with D.O.T. non-shrink grout or BENTOSEAL and level with monolithic concrete surface.

Concrete work shall use conventional cast-in-place forms that produce a smooth surface. Do not use stay-in place concrete forming; use removable forming products only.

All integrated columns/pilaster shall have the waterproofing membrane vertically oriented starting 150 mm (6”) beyond the width of the column/pilaster location to each side.

For below grade expansion joints between 50 mm – 125 mm (2”-5”) in width, install appropriate CETCO CXJ Expansion Joint prior to the installation of the ULTRASEAL AB Waterproofing System.  Only CETCO CXJ Expansion Joint products are eligible for warranty inclusion. Refer to CETCO CXJ Expansion Joint guidelines for expansion joint installation instructions.

<Related work to be completed under Division 3. One (1) row of CETINJECT Injectable Waterstop and one (1) row of WATERSTOP-RX shall be installed in the base wall to slab or footing joint. Two (2) rows of WATERSTOP-RX shall be installed in all other shotcrete construction joints. WATERSTOP-RX shall be installed around applicable penetrations and structural members. Refer to ULTRASEAL Waterproofing Shotcrete Product Manual, CETINJECT Technical Data Sheet, and Waterstop Addendum to VOLTEX DS and ULTRASAL AB Waterproofing systems shotcrete property line foundation walls for further installation procedures and guidelines.>

PREPARATION

Remove dirt, debris, oil, grease, cement laitance, or other foreign matter which will impair or negatively affect the performance of the waterproofing and drainage system.

Protect adjacent work areas and finish surfaces from damage or contamination from waterproofing products during installation operations.

GENERAL INSTALLATION GUIDELINES

Property Line Walls: Install ULTRASEAL AB membrane with adhesive bond coating side in the direction to receive concrete pour; poly liner side outward against installed drainage composite. Overlap ULTRASEAL AB membrane edges minimum 150 mm (6”) and secure with washer-head fasteners placed minimum 600 mm (24”) on center.

Secure center line of ULTRASEAL AB sheets to shoring wall with washer-head fasteners as required to hold membrane tight against shoring wall.

Underslab, install ULTRASEAL AB with the adhesive bond coating side facing installer. Overlap ULTRASEAL AB membrane edges minimum 100 mm (4”).

Backfilled Walls and Earth Covered Structures, install ULTRASEAL AB with poly liner facing installer, overlap ULTRASEAL AB membrane edges a minimum 50 mm (2”) and tape overlaps with CETCO SEAMTAPE.

Expansion Joints: ULTRASEAL AB waterproofing is not an expansion joint filler or sealant but can be incorporated with the CETCO CXJ Expansion Joint to create a warranty eligible, solution for waterproofing the below grade expansion joint. Please refer to the CETCO CXJ Expansion Joint Installation Guide for installation instructions.

AQUADRAIN DRAINAGE COMPOSITE

At the base of the lagging wall, install AQUADRAIN 100BD base-drain horizontally oriented with the open core edge up and the 50 mm (2”) fabric flap side away from the lagging wall. Secure the bottom edge of 100BD to the lagging wall with washer-head fasteners every few feet. Use couplers and corner fittings, as required, to form a continuous 100BD installation. Install discharge outlet fittings to connect with discharge pipes as required for the project. Weep discharge pipes stubbed into 100BD or AQUADRAIN sheet without proper discharge connection fittings are not acceptable.

Install the bottom course of AQUADRAIN 15XP sheet drainage (geotextile side against the lagging wall) with the 15XP bottom edge fabric flap tucked behind the top edge of the 100BD against the lagging to prevent the passage of soil into the core at the connection. Bottom edge of 15XP core should be in contact with open top core edge of 100BD. Place the 50 mm (2”) fabric flap of the 100BD over the back of the 15XP core and secure it with tape to maintain flap position. Secure the top edge of 100BD to the lagging wall with washer-head fasteners 600 mm (24”) on center.

Install subsequent courses of AQUADRAIN 15XP sheet drainage to within 300 mm (12”) of finished grade or as shown on the project drawings. Tightly abut adjoining sheet drain core edges and tuck the extra fabric flaps behind the adjacent roll edge to prevent soil from entering the sheet drain. Secure sheet drain to lagging wall with washer-head fasteners. Where drainage sheet panels are installed overlapped, bottom edge of higher course shall be installed to the outside of the lower course to shed water like a roof shingle.

Prior to installing drainage composite near grade, install 12 mm (½”) thick cementitious wall board centered over metal soldier pile from finished grade elevation to specified depth of soldier pile removal. Cementitious wall board will protect drainage and waterproofing when top of soldier pile is excavated and removed. Remove cementitious board with removal of soldier pile top and lagging.

Around penetrations and tie-back heads, cut sheet drainage composite to fit and wrap extra filter fabric around open core edge to prevent soil from entering core.

At the top of the sheet drain installation, wrap the filter fabric flap behind the exposed top core edge to prevent intrusion of soil into the core and secure sheet drain to wall with termination bar fastened 300 mm (12") on center with the fabric wrapped.

SLAB TO ZERO-LOT LINE SHORING WALL TRANSITION COURSE INSTALLATION

At base of shoring wall, install a ULTRASEAL AB corner transition sheet horizontally oriented (poly liner side against shoring wall; adhesive bond coating side facing installer) with the bottom edge extending out onto the horizontal substrate a minimum 300 mm (12") and the top edge of the sheet extending a minimum 300 mm (12") above the finished slab elevation. Secure ULTRASEAL AB sheet to shoring wall with washer-head fasteners maximum 600 mm (24") on center. Overlap edges of ULTRASEAL AB sheets a minimum 150 mm (6").

If the slab thickness is greater than 600 mm (24"), install a second full sheet horizontally oriented (or more if needed) or cut strip of ULTRASEAL AB horizontally oriented on the shoring wall to meet the 300 mm (12") requirement above of the top slab elevation. Overlap top edge of previous sheet and edges of adjacent sheets a minimum 150 mm (6"). Do not orient overlapped edges of ULTRASEAL AB along the slab to wall joint at the finished slab elevation.

UNDER SLAB INSTALLATION

Reinforced structural foundation slabs should be a minimum of 150 mm (6") thick when placed on a working mud slab. Reinforced concrete slab(s) on compacted grade shall be a minimum of 100 mm (4”) thick. Install ULTRASEAL AB under all footings, elevator pits and grade beams when hydrostatic conditions exist or are anticipated per the historical high ground water elevation reported in the project’s geotechnical documents.

Install underslab ULTRASEAL AB membrane extending to base of shoring wall or interior edge of footing/slab (adhesive bond coating side facing installer) fully overlapping the 12” (300 mm) horizontal tail of the ULTRASEAL AB corner transition sheet previously installed. Secure corner edge of membrane with washer-head fasteners or pneumatic staples 12” (300 mm) on center.

Place ULTRASEAL AB directly on properly prepared substrate (adhesive bond coating side facing installer) with adjoining edges overlapped a minimum of 100 mm (4”). Stagger sheet end seams a minimum of 300 mm (12”). Mechanically fasten or staple ULTRASEAL AB 450 mm (18”) on center to prevent movement from construction operations or concrete placement. When the slab is poured in sections, extend ULTRASEAL AB a minimum 300 mm (12") beyond the slab edge to enable proper overlapping.

Install waterproofing system at all grade beams, pile caps, and other detail areas in accordance with manufacturers detail(s) for specific project condition(s).

Slab Penetrations: For all pipe, rebar, structural or other penetrations install waterproofing system in accordance with manufacturer’s standard detail(s) for specific project condition(s). Ensure no braided or twisted cable penetrate through the waterproofing.

Inspect finished ULTRASEAL AB installation and repair any damaged material prior to concrete slab placement.

WOOD LAGGING WALL INSTALLATION

Starting at the base corner, install base course of ULTRASEAL AB (horizontally oriented) to lagging wall over the previously installed AQUADRAIN and ULTRASEAL AB corner transition course. Overlap ULTRASEAL AB membrane edges minimum 150 mm (6”) and secure with washer-head fasteners placed minimum 600 mm (24”) on center.

Secure center line of ULTRASEAL AB sheets to shoring wall with washer-head fasteners as required to hold membrane tight against shoring wall.

After the bottom horizontal course, ULTRASEAL AB sheets can be installed either vertically or horizontally oriented. Continue ULTRASEAL AB installation up wall to finished grade elevation detail, staggering all sheet roll ends of adjacent courses a minimum 300 mm (12"). Do not allow horizontal ULTRASEAL AB overlap joints to run at same elevation as the shotcrete lift joints; extend membrane past a minimum 150 mm (6”).

Integrated Columns/Pilasters: Install ULTRASEAL AB vertically oriented starting 150 mm (6”) beyond the width of the column/pilaster location to each side.

Tie-Back Heads: For all tie-back heads and soil nails, install waterproofing system with applicable size TB-BOOT in accordance with manufacturer’s detail for specific project condition(s). For irregular shoring wall conditions at tiebacks or oversize tie-back heads consult manufacturer for alternate detail(s) for specific project condition(s).

Penetrations: For all pipe, rebar, structural and other penetrations install waterproofing system in accordance with manufacturer’s detail for specific project condition(s). Ensure no braided or twisted cable penetrate through the waterproofing.

Rebar Anchorage: Install AKWASWELL 9 mm (3/8") thick around all rebar anchorage penetrating ULTRASEAL AB. Then install a length of WATERSTOP-RX around the shaft of the rebar anchorage tight against the BENTOSEAL.

Inspect finished ULTRASEAL AB installation and repair any damaged material prior to shotcrete placement. Ensure ULTRASEAL AB overlap is not separated during shotcrete placement.

METAL SHEET PILING RETENTION WALLS

Any areas of water seepage at the interlocks can be sealed prior to AQUADRAIN installation by injecting BENTOGROUT to the outside of the sheet piling interlocks.

For metal sheet piling shoring walls, first install the ULTRASEAL AB corner transition sheet horizontally oriented with the bottom edge extending minimum 300 mm (12”) out onto the substrate. Cut the bottom edge of the corner transition sheet at piling transition angles to allow the bottom edge to lay flat onto the substrate. Pour 38 mm (1 1/2") continuous cant of WATERSTOPPAGE (alternately install HYDROBAR TUBES) along base of shoring wall. Then install underslab ULTRASEAL AB sheet cut to fit contours of metal sheet piling.

Starting at the base corner, install course of ULTRASEAL AB (horizontally oriented) to metal sheet piling wall over the previously installed AQUADRAIN and ULTRASEAL AB corner transition course. Secure sheet edges to shoring wall with washer-head fasteners placed a maximum 600 mm (24") on center around sheet edge.

After the bottom horizontal course, ULTRASEAL AB sheets can be installed either vertically or horizontally oriented. Continue ULTRASEAL AB installation up wall to finished grade elevation detail, staggering all sheet roll ends of adjacent courses a minimum 300 mm (12"). Do not allow horizontal ULTRASEAL AB overlap joints to run at same elevation as the concrete pour lift joints; extend membrane past a minimum 150 mm (6”). Overlap adjacent ULTRASEAL AB sheet edges a minimum 150 mm (6”).

Integrated Columns/Pilasters: Install ULTRASEAL AB vertically oriented starting 150 mm (6”) beyond the width of the column/pilaster location to each side.

Tie-Back Heads: For all tie-back heads and soil nails, install waterproofing system with applicable size TB-BOOT in accordance with manufacturer’s detail for specific project condition(s). For irregular shoring wall conditions at tiebacks or oversize tie-back heads consult manufacturer for alternate detail for specific project condition(s).

Penetrations: For all pipe, rebar, structural and other penetrations install waterproofing system in accordance with manufacturer’s detail(s) for specific project condition(s). Ensure no braided or twisted cable penetrate through the waterproofing.

Terminate ULTRASEAL AB membrane 300 mm (12”) below finished grade elevation secured with washer-head fasteners maximum 300 mm (12”) on center and with a tooled bead of CETSEAL or M-2000 to exterior surface of concrete wall. Per manufacturer’s detail for specific project condition(s), install ENVIROSHEET grade flashing to primed concrete substrate with bottom edge overlapping top edge of ULTRASEAL AB membrane minimum 150 mm (6”). Overlap all roll ends a minimum 100 mm (4”) to form a continuous flashing. Height of flashing shall be per project details and specifications. Install a rigid termination bar along the top edge of ENVIROSHEET; fastened maximum 300 mm (12”) on center. Complete grade termination detail with tooled bead of CETSEAL or M-2000 along the top edge, at all penetrations through the flashing, and all exposed overlap seams.

Inspect finished ULTRASEAL AB installation and repair any damaged material prior to concrete placement.

CUT ROCK FACE, AUGER CAST CAISSON, OR SHOTCRETE SHORING WALLS:

Cut rock face, auger cast caisson, or shotcrete shoring walls should be sufficiently planar to provide adequately smooth surface to apply AQUADRAIN and ULTRASEAL AB. ULTRASEAL AB will conform to large gradual change in planes (e.g., around caisson column) but should not be installed over sharp surface deflections or voids. Deflections/voids should be filled with cementitious material to create suitable substrate for waterproofing installation.

Install AQUADRAIN drainage composite over cut rock, auger cast caisson, or shotcrete shoring walls per section 3.4.

Install ULTRASEAL AB wall transition course at base of cut rock, auger cast caisson, or shotcrete shoring walls per section 3.5.

Starting at the base corner, install course of ULTRASEAL AB (horizontally oriented) to the shoring wall over the previously installed AQUADRAIN and corner transition course. Secure sheet edges to shoring wall with washer-head fasteners placed a maximum 600 mm (24") on center around sheet edge. Overlap adjacent ULTRASEAL AB sheet edges a minimum 150 mm (6”).

After the bottom horizontal course, ULTRASEAL AB sheets can be installed either vertically or horizontally oriented. Continue installation up wall to finished grade elevation detail, staggering all sheet roll ends of adjacent courses a minimum 300 mm (12"). Do not allow horizontal ULTRASEAL AB overlap joints to run at same elevation as the concrete pour lift joints; extend membrane past a minimum 150 mm (6”). Overlap adjacent ULTRASEAL AB sheet edges a minimum 150 mm (6”).

Integrated Columns/Pilasters: Install ULTRASEAL AB vertically oriented starting 150 mm (6”) beyond the width of the column/pilaster location to each side.

Tie-Back Heads: For all tie-back heads and soil nails, install waterproofing system with applicable size TB-BOOT in accordance with manufacturer’s detail for specific project condition(s). For irregular shoring wall conditions at tiebacks or oversize tie-back heads consult manufacturer for alternate detail for specific project condition(s).

Penetrations: For all pipe, rebar, structural and other penetrations install waterproofing system in accordance with manufacturer’s detail for specific project condition(s). Ensure no braided or twisted cable penetrate through the waterproofing.

Terminate ULTRASEAL AB membrane 300 mm (12”) below finished grade elevation secured with washer-head fasteners maximum 300 mm (12”) on center and with a tooled bead of CETSEAL or M-2000 to exterior surface of concrete wall. Per manufacturer’s detail for specific project condition(s), install ENVIROSHEET grade flashing to primed concrete substrate with bottom edge overlapping top edge of ULTRASEAL AB membrane minimum 150 mm (6”). Overlap all roll ends a minimum 100 mm (4”) to form a continuous flashing. Height of flashing shall be per project details and specifications. Install a 25mm x 3mm (1” x 1/8”) rigid aluminum or stainless-steel termination bar along the top edge of ENVIROSHEET; fastened maximum 300 mm (12”) on center. Complete grade termination detail with tooled bead of CETSEAL or M-2000 along the top edge, at all penetrations through the flashing, and all exposed overlap seams.

Inspect finished ULTRASEAL AB installation and repair any damaged material prior to concrete placement.

EXCAVATION, GRADE TERMINATION AND BACKFILL

Coordinate with excavation and backfill operations conducted under Division 31 Work to remove the top few wood lagging timbers and top end of the metal soldier piles per local building code or project requirements. Identify and repair any waterproofing and drainage sheet damaged by excavation and removal of soldier pile heads and lagging. Where excavated, fasten all exposed ULTRASEAL AB overlap seams maximum 600 mm (24”) on center and apply CETCO SEAMTAPE centered along overlap seams.

Terminate ULTRASEAL AB membrane 300 mm (12”) below finished grade elevation secured with washer-head fasteners maximum 300 mm (12”) on center and with a tooled bead of CETSEAL or M-2000 to exterior surface of concrete wall. Per manufacturer’s detail for specific project condition(s), install ENVIROSHEET grade flashing to primed concrete substrate with bottom edge overlapping top edge of ULTRASEAL AB membrane minimum 150 mm (6”). Overlap all roll ends a minimum 100 mm (4”) to form a continuous flashing. Height of flashing shall be per project details and specifications. Install a 25mm x 3mm (1” x 1/8”) rigid aluminum or stainless-steel termination bar along the top edge of ENVIROSHEET; fastened maximum 300 mm (12”) on center. Complete grade termination detail with tooled bead of CETSEAL or M-2000 along the top edge, at all penetrations through the flashing, and all exposed overlap seams.

Backfill shall be placed and compacted to minimum 85% Modified Proctor Density promptly after waterproofing has been installed. Closely coordinate with contractor responsible for backfill work by informing them each time a waterproofed area is ready for backfill. Backfill shall consist of compactable soil or angular aggregate 20 mm (¾”) or less and free of debris and sharp objects. Care should be used during backfill operation to avoid damage to the waterproofing system. If damage occurs, cease backfilling and report damage. Damaged waterproofing must be repaired per manufacturer’s guidelines.

CLEAN UP

In areas where adjacent finished surfaces are soiled by work of this Section, consult manufacturer of surfaces for cleaning advice and conform to their recommendations and instructions. Remove all tools, equipment and remaining product on-site. Dispose of section work debris and damaged product following all applicable regulations.

END OF SECTION

# Text boxes

This guide specification was issued January 2021 and may be superseded without notice at any time. Therefore, please confirm that this specification is still current and has not been superseded by checking at www.cetco.com or by calling CETCO at 1-847-851-1800.

SHOTCRETE CONSTRUCTION SPECIFICATION

This guide specification has been prepared according to the principles established in the Manual of Practice published by the Construction Specification Institute and is intended for use with below-grade structural shotcrete foundation walls. This specification is not intended for use with masonry block or precast concrete construction. Contact CETCO regarding installation guidelines for applications not covered herein. CETCO, Building Materials Group – (847) 851-1800.